## Slide 1: Semantics-enabled Connectivity: Configuring Time Sensitive Networking (TSN) from W3C WoT Thing Description (TD)
Luca Sciullo and Matthias Kovatsch
T2TRG / W3C WoT Meeting, Singapore, 15 Nov 2019

## Slide 2: Background: TSN and OPC UA for IIoT
Industrial IoT often requires determenistic networking  Plethora of field buses and complex wireless standards (cf. 6TiSCH…)
Connectivity between applications requires network configuration!

## Slide 3: OPC UA Field Level Communications
New
Available
OPC UA: So far, mainly a management interface for configuration and diagnostics
FLC activity: OPC UA to become also a field-level standard for cross-vendor interoperability
FLC Focus: Controller-to-Controller (and later -Device)

## Slide 4: OPC UA Example (UAExpert Browse View)
Information Model roughly similar to the Web
Browsing
Nodes (~resources)
  Namespace (URI mapped to integer)
  Identifier
    Integer
    String
    Binary
    GUID
  Class
    Object
    Variable
    Method
    Reference
    Various type classes
Bidirectional references, bitmaps, word sizes, ...

## Slide 5: OPC UA FLC as W3C WoT Binding
OPC UA FLC
OPC UA Server plus PubSub
Functional Entity (FLC)
Variables
Methods
Published DataSets
Server addr, namespace, NodeID
W3C WoT
Servient
Thing
Properties
Actions
Events
Form href

## Slide 6: IEEE Time-Sensitive Networking (TSN)
.1AS (-rev)
1588 PTP
.1Qci
802.1Q
.1Qbv
.1Qcr
.1Qcc
.1Qbu
.1Qdd
.1Qca
.1Qdj
IEEE family of specification for deterministic networking
Extends 802.1Q VLAN standard (makes use of VLAN tagging)
Enables scheduled traffic, i.e., deterministic time slots, latency, and jitter for selected traffic
Allows for the convergence of many fieldbus technologies into a standard Ethernet network

## Slide 7: Time-Aware Scheduler and Gate Control Lists
non-TSN
TSN
non-TSN
TSN
non-TSN
non-TSN
non-TSN
Gate
Gate
Gate
Gate
Transmission Selection
Prio 7
Queue 7
Prio 6
Q. 6
Q. 5
Q. 0
Best Effort
...
Gate
Gate
Gate
Gate
Transmission Selection
Prio 7
Gate 7
Prio 6
Gate 6
Gate 5
Gate 0
Best Effort
...
T0: Occccccc
T1: ccOOOOOO
T2: cOcccccc
T3: ccOOOOOO
Bandwidth guarantee
Latency/deadline guarantee

## Slide 8: Network Configuration (Centralized Model)
Network configuration usually done via YANG modules (cf. CoRECONF for LP-WAN work)
Multiple protocol choices for industry
  NETCONF
  RESTCONF
  CoRECONF
Network equipment mainly has NETCONF interfaces

## Slide 9: NETCONF as W3C WoT Binding
NETCONF
Embedded stack on device
NETCONF datastores
Leaf nodes
RPCs (other than get/edit-config)
Notifications
X-Path
W3C WoT
Servient
Thing
Properties
Actions
Events
Form href (part)

## Slide 10: NETCONF Examples
Read Property
<rpc ...attributes...>
<get>
<filter type="subtree">
<...path to leaf...>
</...path to leaf...>
</filter>
</get>
</rpc>
Write Property
<rpc ...attributes...>
<edit-config>
<target>
<running/>
</target>
<config>
<...path to leaf...>
... Configuration data ...
</...path to leaf...>
</config>
</edit-config>
</rpc>

## Slide 11: Discussion of Design Decisions: NETCONF
Multiple datastores (Startup, Running, Candidate)
  Multiple Things (one per store)? No, need address info in form anyway
  Multiple Properties per leaf?
    URI-Template? (No, info not part of path)
    Form term to select (nc:target)?
      Also needs target as application metadata (at Property level)
  Multiple forms per store? (No, all forms must be equivalent)
Batch changes and commit RPCs
  writemultipleproperties Interaction? (No, would make commit implicit)
  Application metadata and commit Action?
Custom RPCs
  Form method field is open set (parameter passed to Binding)

## Slide 12: Discussion of Design Decisions: OPC UA
OPC UA Binding requires detailed type information (e.g., word size)
  Have info in Content-Type parameter? No, does not work for complex types
  Extend DataSchema with new term (opc:datatype)
    DataSchema needs to be passed to Binding (not only form metadata)
Custom data types in OPC UA are used often and blow up TD
  Just inline and live with it?
  Mechanism to declare once and reference? (cf. $ref feature of JSON Schema)
URI definition
  HTTP style with query?  opc.tcp://host.local:4841/?ns=3&i=4711
  OPC style from existing tools?  opc.tcp://host.local:4841/ns=3;i=41711
Historic access
  Properties with URI-Template? No, getting too complex...
  Action?

## Slide 13: Semantics-enabled Connectivity through TDs
Sensor
(I/O Module)
Actuator
Transport System
Position
Servient
OPC UA
Data Model
WoT Runtime
Scripting API
NETCONF
PLC Mashup App
TSN Controller App
* Currently no TSN-enabled end devices available
③
① Fetch TDs with QoS capabilities
①
①
Match with QoS requirements ②
⑤
Request configuration
Confirm / Reject
④ Try to push out schedule

## Slide 14: QoS Capabilities and Requirements
Capabilities of Things (sometimes req.)
Minimum interval
Message sizes
Send offset (e.g., sensor reading ... sending)
Receive offset (e.g., Action invocation)
Clock synchronization
Requirements of Apps
Maximum interval
Overall delay
Receive offset (jitter)
Currently being collected and mapped to new TD vocabulary

## Slide 15: New TD Vocabulary for QoS, but there is more
Works for Things (illustration TD)
{
"@context": [
"https://www.w3c.org/2019/wot/td/v1",
{ "qos": "https://example.org/qos-vocab-v1" }
],
"@type": ["Thing"],
"name": "MyRobot",
"securityDefinitions": {
"default": {
"scheme": "bearer"
}
},
"qos:clockSyncrhonization": "as-rev",
"qos:minInterval": 31.25, // microseconds enough? nano? How many .zeros
"actions": {
"goto": {
"qos:receiveOffset": 2.3,
"input": {
"type": "object",
...
}, "form": [
"qos:maxFrameSize": 127,
...
]
}
}
}
How to better describe apps?
Only Scripting API potential standard
Currently no container format
Apps may also have requirements
Related work
  OSGi Requirements and Capabilities
  Network Function Virtualization

## Slide 16: Related Work
QoS information in TDs just one way to do it
  Builds on cross-application capabilties of W3C WoT
  TSN configuration not only for OPC UA FLC
  TSN is for a converged network
  Other applications are also expected to provide QoS requests
CUC became part of mashup app
CNC implemented as app + Binding
IEEE 802.1Qcc has abstract concept of CUC and CNC
  Application protocol to communicate QoS request to CUC
  CUC informs CNC through standard interface (t.b.d. in .1Qdj)
  CNC rolls out TSN configuration using NETCONF / YANG
OPC UA TSN Sub-group proposes PubSub TSN Centralized Configuration (PTCC)

## Slide 17: Conclusions
TSN converges IIoT connectivity (wired, which are 94% of fieldbuses)
  Application QoS requests have to be converted into TSN configuration
  TSN for WLAN and TSN abstractions for 5G under development
TDs can semantically model QoS requirements and capabilities
  Initial proposal and proof of concept in upcoming paper
  Need also a description mechanism for apps
Many design choices for W3C WoT Bindings
  Many trade-offs for complex/traditional ecosystem standards
  Upcoming paper will give guidance based on OPC UA and NETCONF

## Slide 18: Other Points
Why mainly RESTCONF support on devices?
  Myth of RESTCONF only being a subset missing features for device?
CoRECONF timeline?
TSN + CoRECONF + CoRE applications a candidate for IIoT?
  Feature set very close to modern industrial fieldbuses
  Could there be an actual industrial revolution?
Real-time NodeJS? Anyone working on this?

## Slide 19: Contact
Luca Sciullo
PhD Student / Visiting Researcher
University of Bologna / Huawei
Dr. Matthias Kovatsch
Principal Researcher
Huawei, Munich Research Center
matthias.kovatsch@huawei.com
(Note that this is a research view)